## Slide 1
Integration, Development and Results of the 500 Teraflop Heterogeneous Cluster (Condor)
11 September 2012
Mark Barnell
Air Force Research Laboratory

## Slide 2: Agenda
Mission
RI HPC-ARC & HPC Systems
Condor Cluster
Success and Results
Future Work
Conclusions

## Slide 3
1995
2000
2005
2010
SKY (PowerPC)
200 GFLOPS/$M
10
100
INTEL PARAGON (i860) 12 GFLOPS/$M
1,000
10,000
1M
Heterogeneous HPC
XEON + FPGA
81 TOPS/$M
53 TFLOP Cell Cluster
147 TFLOPS/$M
500 TFLOP Cell-GPGPU
250 TFLOPS/$M
Exponentially Improving Price-Performance
Measured by AFRL-Rome HPCs
100,000
15 years, 20,000X
Roughly 2n
Commodity
Embedded
Servers
FPGAs
Gaming
Multicore
GPGPU

## Slide 4: Agenda
Mission
RI HPC-ARC & HPC Systems
Condor Cluster
Success and Results
Future Work
Conclusions

## Slide 5: Mission
Objective: To support CS&E R&D along with HPC to the Field experiments by providing interactive access to hardware, software and user services with special attention to applications and missions supporting C4ISR.
Technical Mission: Provide classical and unique, real-time, interactive HPC resources to the AF and DoD R&D community.

## Slide 6
Mission
RI HPC-ARC & HPC Systems
Condor Cluster
Success and Results
Future Work
Conclusions

## Slide 7: HPC Facility Resources
CONDOR CLUSTER
500 TFLOPS
Funding: $2M HPCMP DHPI
Urban Surveillance
Cognitive Computing
Quantum Computing
Cell BE Cluster
53 TFLOPS Peak
Performance
EMULAB
Network Emulation
Testbed
HORUS
22TFLOPS TTCP
Field Experiments
1
Dual 10 GbE
Infiniband
40 Gb/s
1 GbE
2
Dual 10 GbE
Infiniband
40 Gb/s
1 GbE
3
Dual 10 GbE
1 GbE
84
Dual 10 GbE
Infiniband
40 Gb/s
1 GbE
HPC Assets on
HPC DREN Network
HPC SDREN Assets
May 2012
Legend:
Online: Nov 2010

## Slide 8: HPC Facility Resources GPGPU Clusters
CONDOR CLUSTER
500 TFLOPS
Funding: $2M HPCMP DHPI
Urban Surveillance
Cognitive Computing
Quantum Computing
HORUS
22TFLOPS TTCP
Field Experiments
1
Dual 10 GbE
Infiniband
40 Gb/s
1 GbE
2
Dual 10 GbE
Infiniband
40 Gb/s
1 GbE
3
Dual 10 GbE
1 GbE
84
Dual 10 GbE
Infiniband
40 Gb/s
1 GbE
HPC GPGPU Assets on DREN Network
Legend:
Online: Nov 2010
ATI Cluster
32 TFLOPS ATI
FirePro 8800
Online: Jan 2011
Upgrade all Nvidia GPGPUs to C2050s & C2070s Tesla cards June 2012
30 Kepler cards ~90K will have a 3x improvement (1.5Tflop DP) 220W
  Condor among the greenest HPC in the world (1.25 Gflop/W DP&SP)
Redistribute 60 C1060 Tesla cards to other HPC and research sites
  ASIC, UMASS, & ARSC

## Slide 9
Mission
RI HPC-ARC & HPC Systems
Condor Cluster
Success and Results
Future Work
Conclusions

## Slide 10: The Condor Cluster
1716 SONY Playstation3s
STI Cell Broadband Engine
  PowerPC PPE
  6 SPEs
  256 MB RAM
84 head nodes
6 gateway access points
78 compute nodes
  Intel Xeon X5650 dual-socket hexa-core
  (2) NVIDIA Tesla GPGPUs
    54 nodes – (108) C2050
    24 nodes – (48) C2070/5
  24-48 GB RAM
FY10 DHPI
Key design considerations: Price/performance & Performance/Watt

## Slide 11: Condor Cluster (500 Tflops)
263 Tflops from 1,716 PS3s
    153 GFLOPS/PS3
    78 subclusters of 22 PS3s
225 Tflops from server nodes
    84 sever nodes (Intel Westmere 5650 dual socket Hexa (12 cores))
    Dual GPGPUs in 78 server nodes
    Firebird Cluster (~32 Tflops)
Cost: Approx. $2M
Sustained throughput benchmarks/appications YTD: Xeon X5650: 16.8 Tflops, Cell 171.6 Tflops, C2050 : 68.2 Tflops, C2070: 34 Tflops….CONDOR TOTAL 290.6 Tflops
1
Dual 10 GbE
1 GbE
2
Dual 10 GbE
1 GbE
3
Dual 10 GbE
1 GbE
84
Dual 10 GbE
1 GbE
Online: November 2010
Infiniband
40 Gb/s
Infiniband
40 Gb/s
Infiniband
40 Gb/s

## Slide 12: Condor Cluster Networks
10 GbE STAR-Bonded HUB
Switch
Rack2
Switch
Switch
Rack4
Rack1
Switch
Rack6
Switch
DELL RACK
Rack3
Switch
Switch
Rack5
Switch
Switch
Server
CS15
CS16
CS17
CS18
CS19
CS20
CS21
CS22
CS23
CS24
CS25
CS26
CS27
Server
CS29
CS30
CS31
CS32
CS33
CS34
CS35
CS36
CS37
CS38
CS39
CS40
CS41
CS28
CS42
BOND
BOND
BOND
BOND
BOND
Server
CS57
CS58
CS59
CS60
CS61
CS62
CS63
CS64
CS65
CS66
CS67
CS68
CS69
CS70
Server
CS71
CS72
CS73
CS74
CS75
CS76
CS77
CS78
CS79
CS80
CS81
CS82
CS83
CS84
Server
CS1
CS2
CS3
CS4
CS5
CS6
CS7
CS8
CS9
CS10
CS11
CS12
CS13
CS14
Server
CS43
CS44
CS45
CS46
CS47
CS48
CS49
CS50
CS51
CS52
CS53
CS54
CS55
CS56
Server
CPS40
CPS41
CPS42
CPS43
CPS44
CPS45
CPS46
CPS47
CPS48
CPS49
CPS50
CPS51
CPS52
CPS53
Server
CPS53
CPS54
CPS55
CPS56
CPS57
CPS58
CPS59
CPS60
CPS61
CPS62
CPS63
CPS64
CPS65
Server
CPS66
CPS67
CPS68
CPS69
CPS70
CPS71
CPS72
CPS73
CPS74
CPS75
CPS76
CPS77
CPS78
Switch
Switch
Server
CPS1
CPS2
CPS3
CPS4
CPS5
CPS6
CPS7
CPS8
CPS9
CPS10
CPS11
CPS12
CPS13
Server
CPS27
CPS28
CPS29
CPS30
CPS31
CPS32
CPS33
CPS34
CPS35
CPS36
CPS37
CPS38
CPS39
Switch
BOND
Server
CPS14
CPS15
CPS16
CPS17
CPS18
CPS19
CPS20
CPS21
CPS22
CPS23
CPS24
CPS25
CPS26
S
W
I
T
C
H
S
S
W
I
T
C
H
S
S
W
I
T
C
H
S
W
I
T
C
H
S
x13
x13
x22
x22
x22
x22
x22
x22
x14
x13
x13
x14
x13
x14
x14
x13
x14
x14

## Slide 13: Condor Cluster Networks
Infiniband Mesh Non-Blocking 20Gb/s
(5) 12200 & (1) 12300 Qlogic 40Gb/s Infiniband (36 port) switches
B
24
5
36
Rack 6 14
servers
14
4
10
Rack 4 14
servers
14
Rack 3 14
servers
14
Rack 2 14
servers
4
6
6
6
6
Rack 1 14
servers
14
6
6
6
6
6
32
A
24
4
32
3
28
Rack 5 14
servers

## Slide 14: Condor Web Interface

## Slide 15
Mission
RI HPC-ARC & HPC Systems
Condor Cluster
Success and Results
Future Work
Conclusions

## Slide 16: Solving Demanding, Real-Time Military Problems
Radar processing for high resolution images
Occluded text recognition
Space object identification
…but beginning to perceive that the handcuffs were not for me and that the military had so far got….

## Slide 17: RADAR Data Processing for High Resolution Images
Radar processing for high resolution
images in real-time

## Slide 18: Optical Text Recognition Processing Performance
Computing resources involved in this run
  4 Condor servers – 32 Intel Xeon processor cores
  88 PlayStation 3’s – 616 IBM Cell-BE processor cores
  40 Condor servers – 320 Intel Xeon processor cores
  880 PS3s – 6160 IBM Cell-BE Processor cores (21 pages/sec)

## Slide 19: Space Object Identification
Low resolution frames
High resolution image
Combining frames to create high quality
images in real-time

## Slide 20: Matrix Multiply
Matrix-matrix multiplication test
C2050 (MAGMA vs CUBLAS)
Chart: 
| 1024 | 2048 | 3072 | 4096 | 5120 | 6144 | 7168 | 8192 | 9216 | 10240
Magma | 547.41 | 596.09 | 637.42 | 633.46 | 630.93 | 648.55 | 643.72 | 639.47 | 649.6 | 646.15
CUBLAS | 447.39 | 588.35 | 632.14 | 613.31 | 628.82 | 642.62 | 626.47 | 634.67 | 643.61 | 632.84
GFLOPS
Matrix Size
Chart: 
| 1024 | 2048 | 3072 | 4032 | 5184 | 6016 | 7040 | 8064 | 9088 | 10112
Intel 5650 12 Cores | 23.57 | 139.95 | 151.54 | 163.66 | 167.42 | 171.55 | 199.86 | 202.13 | 207.65 | 210.34
Nvidia C2050 | 29.99 | 90.83 | 152.28 | 278.75 | 330.98 | 355.83 | 377.77 | 403.77 | 421.49 | 434.3
Matrix Size
GFLOPS
MAGMA-only, one-sided matrix factorization

## Slide 21
Condor/Firebird provides access to next-generation hybrid CPU/GPU architectures
  Critical for understanding the capability and operation prior to larger deployments
  Opportunity to study non-traditional applications of HPC, e.g., C4I applications
CPU/GPU compute nodes provides significant raw computing power
  OCL N-Body benchmark with 768K particles sustained performance ~ 2 TFLOPS using 4 Tesla C2050s or 3 FireBird V8800s
Production chemistry code (LAMMPS) shows speedup with minimal effort
  Original CPU code ported to OpenCL with limited source code modifications
  Exact double-precision algorithm runs on Nvidia and AMD nodes
  Overall platform capability increased by 2x (2.8x) without any GPU optimization
LAMMPS-OCL EAM Benchmark2
(Absolutely no GPU optimizations)
Xeon X5660
FirePro V8800
Tesla C2050
2
4
8
1
2
2
3
4
1
3
1
(cores)
(GPUs)
(GPUs)
OpenCL N-Body Benchmark1
1 GPU
2 GPUs
3 GPUs
4 GPUs
Tesla C2050
FirePro V8800
1MPI-modified BDT N-Body benchmark distributed with COPRTHR 1.1
2LAMMPS-OCL is a modified version of the LAMMPS molecular dynamics code ported to OpenCL by Brown Deer Technology
LAMMPS on GPUs

## Slide 22
Mission
RI HPC-ARC & HPC Systems
Condor Cluster
Success and Results
Future Work
Conclusions

## Slide 23: Future Work
Improved OTR applications
  Multiple languages
Space Situation Awareness
  Heterogeneous algorithms
Persistent Wide Area Surveillance

## Slide 24: Autonomous Sensing in Persistent Wide-Area Surveillance
Cross-TD effort
  Investigate scalable, real-time and autonomous sensing technologies
  Develop a neuromorphic computing architecture for synthetic aperture radar (SAR) imagery information exploitation
  Provide critical wide-area persistent surveillance capabilities including motion detection, object recognition, areas-of-interest identification and predictive sensing

## Slide 25: Conclusions
  Valuable resource to support entire AFRL/RI, AFRL and tri-service RDT&E community.
  Leading large GPGPU development and benchmarking tests.
  This investment is leveraged by many (130+) users
  Technical benefits – Faster, higher fidelity problem solution; multiple parallel solutions, heterogeneous application development

## Slide 26
Questions?