## Slide 1: Multithreaded FPGA Acceleration of DNA Sequence Mapping
Edward Fernandez, Walid Najjar, Stefano Lonardi, Jason Villarreal
UC Riverside, Department of Computer Science and Engineering
Jacquard Computing

## Slide 2: Introduction
Multithreaded architectures masks long memory latencies by context switching threads.
FPGA provides a platform for hardware acceleration of multithreaded architectures targeting a specific application
Our target application for this research is DNA sequence matching

## Slide 3: Introduction
FHAST (FPGA Hardware Accelerated Sequencing Tool) implements a heuristic based on the FM-Index string matching algorithm
FHAST is implemented on Convey Computer HC-1 which can be used as a drop-in replacement for the Bowtie sequencing tool
Speed up of FHAST compared to Bowtie ranges from 7x to 70x dependent on allowed number of mismatches

## Slide 4: Presentation Outline
FM-Index String Matching Algorithm
Hardware Architecture
  Exact String Matching Architecture
  Approximate String Matching Architecture
Implementation
Results Evaluation
Conclusion

## Slide 5: FM-Index String Matching Algorithm
The FM-index operates on the Burrows-Wheeler Transform of the text
The top and bottom pointers of the FM-index indicate a matching pattern on the text for every character of the pattern processed
  Top >= Bottom: pattern does not exist
  Top < Bottom: pattern exists

## Slide 6: FM-Index String Matching Algorithm
C
T
T
T
A
C
A
G
$
A
G
C
G
T
A
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
Search pattern: T A G G
Text: GCTAATTAGGTACC$
Search pattern: C C G A
C
T
T
T
A
C
A
G
$
A
G
C
G
T
A
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
Top
Bottom
Top
Bottom
PATTERN EXISTS
PATTERN DOES NOT EXISTS

## Slide 7: FM-Index String Matching Algorithm
Limited block RAM available on the FPGA for storing the Burrows-Wheeler Transform (BWT) of an extremely long text
Utilization of external memory to store BWT of the text
Exploitation of multiple threads to masks long latencies because of memory access.

## Slide 8: Multithreading
Memory
Threads wait in queues while waiting for memory to return required data
Multiple threads are processed to achieve parallelism and faster execution
Ready Threads
Waiting Threads

## Slide 9: Exact String Matching Architecture
Receive
Send
Locate
Update
C-Table
(External)
Fetch
Pattern source
(External)
Output file
(External)
A thread represents a pattern in the queue of the components.
Multiple threads are processed to hide latencies due to memory access.

## Slide 10: Approximate String Matching Architecture
Pattern
source
(External)
Engine 0
pattern
Engine 1
….
Engine n
C-Table (External)
Locate
Block
A miss on Engine n creates three new threads and passed to Engine n+1
Each new thread on the succeeding thread replaces the failing base pair with the other three base pairs

## Slide 11: Implementation
Coprocessor call
(Hardware)
Setup registers
Setup input table
Allocate memory
Setup output table
Report output table
C-Table/Suffix Array (External)
Pattern
source
(External)
(Software)
Software: Performs memory allocation for reading the C tables, the suffix arrays, the reads and writing the results to external memory.
Hardware: Executes the search algorithm
Convey HC-1 hybrid core:
Dual core Intel Xeon processor 2.13 GHz
Four Xilinx Virtex 5 FPGAs as coprocessor with eight memory controller supporting peak bandwidth of 80 GB/s at 150 MHz.

## Slide 12: Experimental Setup
18 million unique reads with 101 base pairs on Chromosome 14 of the human genome (length of 107 million base pairs)
Bowtie is executed in the two following setup
 | CPU1 | CPU2
Processor Type | Xeon L540B | Xeon E5520
# of cores | 2 dual cores | 2 quad cores
Memory size | 192 GB | 24 GB
Cache size | 6 MB | 8 MB
Frequency | 2.13 GHz | 2.27 GHz

## Slide 13: Execution Time
Longer execution time of Bowtie running in both CPUs compared to FHAST
Simultaneous searching of the reads in three engines of FHAST results to no significant difference in execution time for difference mismatches
Mismatch | FHAST | Bowtie | 
 |  | CPU1 | CPU2
0 | 55.43 | 715 | 404
1 | 71.17 | 1924 | 1142
2 | 73.25 | 5410 | 3698

## Slide 14: Speed Up
Highest speed up (70x) is achieved in detecting two mismatches where execution time of Bowtie is longest

## Slide 15: Conclusion
We demonstrated a multithreaded approach using FPGAs to accelerate execution of DNA sequence matching
We compared FHAST execution time to Bowtie which is a widely used tool for sequencing reads and showed an actual performance improvement up to 70x

## Slide 16: Thanks for Listening

## Slide 17: Back up slides

## Slide 18: Performance Improvement
New read
Update block
read
Old read
RAM
Old pointer
New pointer
pointer
The memory address are pre-calculated and stored on a RAM for all character combinations up to a specific length such that each combination of characters represent a range.
Instead of initializing the address to the first and last rows of the C-table, we initialize the top and bottom pointers to the pre-calculated values

## Slide 19: Replace Block
Replace: The replace block creates three copies of the failing read and replaces the failing character with the other base pairs.
The update block of Engine 1 accepts reads from replace block instead of
the fetch block.
Read in Engine N
Read in Engine N-1
Update block
Replace
block
read
pointer
Pointer of Read in Engine N-1
Pointer of Read in Engine N

## Slide 20: Scaling Factor
Scaling factor defined as execution time on a single device divided by the number of devices
Results show that FHAST scales better if more FPGAs are used for searching
Chart: Mismatch
| 0 | 1 | 2
FHAST | 3.7525 | 3.8591 | 3.7309
Bowtie | 2.7862 | 2.8128 | 2.1895